Overview of Continuous Controllers (CCs) implemented by Yoshimi
(Full details in the Advanced User Manual)

CC	Function
hex	dec
00	0	Bank change MSB (or LSB)
01	1	Mod wheel
02	2	Breath
…	...
06	6	NRPN data MSB
07	7	Volume
…	…	(x2)
0A	10	Panning
0B	11	Expression
…	…	(x18)
20	32	Bank Change LSB (or MSB)
…	…	(x5)
26	38	NRPN Data LSB
…	…	(x25)
40	64	Sustain pedal
41	65	Portamento
…	…	(x3)
44	68	Legato pedal
…	…	(x2)
47	71	Filter Q
…	…	(x2)
4A	74	Filter Cutoff
4B	75	Bandwidth
4C	76	FM Amplitude
4D	77	Resonance Center Frequency
4E	78	Resonance Bandwith
…	…	(x17)
60	96	NRPN Data Increment
61	97	NRPN Data Decrement
62	98	NRPN LSB
63	99	NRPN MSB
…	…	(x20)
78	120	All Sound Off
79	121	Reset All Controllers
…	...
7B	123	All Notes Off
…	…	(x4)

Non Recognised Parameter Numbers (NRPNs) implemented by Yoshimi

MSB	LSB	Function
hex	dec	hex	dec
04	4	< 05	< 5	System Effect Number
08	4	< 09	< 9	Insertion Effect Number

40	64	00	0	Direct Part Control
40	64	01	1	Vector Control
40	64	02	2	System config settings

60	96	< 6	< 6	Load numbered files from history lists

Shortform types (no data bytes needed – LSB is the data)
41	65	< 6	< 6	Set Solo Switch Type
42	66	< 78	< 120	Set Solo Switch Incoming Controller

44	68	44	68	Perform normal shutdown, exit value of 0
44	68	45	69	Perform shutdown with no messages, exit value of 16