The Short Yoshimi Guide

This guide is intended to get you started making enjoyable sounds without going deeply into each topic. At all times you are encouraged to experiment – you might not get the results you expect but you won’t do any harm.

When using the mouse the left button is generally used. The right button is mostly used for setting defaults or initiating MIDI-learn, but is also used for alternative menu operations. The scroll wheel gives fine control of knobs/sliders. Like many programs, Yoshimi has multiple routes to get to most major functions, but we will only describe the easiest ones here.

Yoshimi remembers the last placement of most windows and these will re-open at the same location. Also, it will remember whether they were open when you last closed Yoshimi itself. The next time you run these will be re-opened.

First startup

The very first time you start Yoshimi you will see the main window and alongside this the virtual keyboard. The main window will also have a small information window overlaying with a couple of recommendations. You will only see this once.

Clicking on the virtual keyboard with the mouse should immediately produce sound, although it will be a plain sine-wave. Yoshimi tries to connect to Jack first, and if it can’t find that it will connect to the Alsa audio server. If it can’t find that either, it will still run (with no output) to give you a chance to investigate what went wrong.

If you got Yoshimi from one of the many distributions that carry it, then as well as the program itself you will get banks of instruments. These are the definition files that program Yoshimi’s sound engines. If you self-built from source you will find these in the ‘yoshimi/banks’ directory. In either case, Yoshimi will hunt for these banks the first time it is started (others can be added later at any time without disturbing these).

Clicking on ‘Simple Sound’ will open a window with a drop-down list at the top left that will show ‘Arpeggios’. This ‘bank’ has instruments you can chose with the mouse, and play on the virtual keyboard. You can use keys as well as mouse, but you do need to click on the virtual keyboard with the mouse first to gain focus.

To see what is in other banks, either use the drop-down list or click on the ‘banks’ button. The list is slightly quicker, but the banks button opens a new window that gives a clearer idea of what is available. Either way, once selected, the current bank window will show the new instruments. Yoshimi remembers the last used bank on your next run.

At this point you will probably want to connect to a real MIDI keyboard (or other source of MIDI).

On first time start Yoshimi defaults to ALSA MIDI but if the server is not available, as with audio, it will try Jack. If you have a hardware soundcard with a MIDI or USB keyboard Yoshimi will usually find this. A program like qjackctl can be used to find and connect these, even if not running Jack, alternatively you will need to open a terminal window and type in:

aconnect --list

This will give you a list of all the possible MIDI clients that are available, and you should recognise your keyboard by its name in quotes. This is followed by a similar line with the available ports.

Now is probably a good time to take a quick look at settings. On the top menu bar, click on ‘Yoshimi’ for the drop-down menu and click on the fifth item ‘Settings...’

For connecting to specific devices , leave the main settings and click on ‘Alsa’. Where it says ‘Connection Type’ change it to ‘Fixed’ and for ‘Alsa MIDI Source, in place of the word “default” type what was inside the quotes (but not the quotes themselves).

Going back to ‘Main Settings’ the default for Internal Buffer Size is actually 256, but if your first-time startup was with Alsa it may be different, typically 1024. If you set it back to 256 then when you save the settings, Alsa will use this size.

To fix your changes click on ‘Save and Close’ and restart Yoshimi for these to take effect. Your settings are now permanently stored.

Parts and Channels

By default, most MIDI sources use channel 1 and this is the channel that Yoshimi first listens to with part 1. However, you can select other parts via the ‘Part’ spinbox and/or change the channel it listens to with the ‘MIDI’ spinbox.

If you click on the ‘Mixer Panel’ button you get a new window that is much more convenient for basic control of parts and their channels. The row of check boxes along the top enable and disable each part. None of the other part controls are active until their enable box is checked. The name field below opens the current instrument bank in the same way as the one in the main window.

Next you have a volume slider and then a panning knob. Again you have a channel selector, but this time it’s a drop-down list. Underneath that is another drop-down list. This is only active if you are using jack audio, and lets you direct the part’s audio to it’s own pair of outputs.

Finally there is the ‘Edit’ button. A mouse click on this simply makes it the current selected part and synchronises the main window to show this. However using the right hand mouse button will actually get you into the sound editors.

Sound Editors.

These can be reached either as mentioned above from the mixer panel or by clicking on the ‘Edit’ button in the main window.

There are three sound engines, AddSynth, SubSynth and PadSynth, corresponding to additive synthesis, subtractive synthesis and Paul Nasca’s own design that creates, then plays, perfectly looping sound samples. These can be used individually, or all together to make more complex sounds. There are check boxes to enable and disable them and ‘Edit’ buttons to enter the editors.

These are quite complex and we will not go into detail in this short guide, but do explore to see and hear the things you can do.

Below these there are a pair of ‘Humanise’ sliders, ‘Detune’ and ‘Velocity’. Detune gives a very small random pitch shift to the entire part, while Velocity gives a random small playing weight change. As well as affecting the apparent volume, it will also modify and velocity sensing parts of Yoshimi, such as filters.

In this group edit window there is also a ‘Kit Edit’ button that allows you to build up things like drum kits or very multi-layered sounds, but the latter need a good fast processor! There is also an ‘Effects’ button that opens a new window with all the effects that can be added to individual parts.

Effects

These fall into three groups. System, Insertion and Part. Tabs for System and Insertion effects are in the middle of Yoshimi’s main window.

System effects apply to the entire output sound, but the amount fed to them is decided per part by the System Effect Sends that are near the bottom right of the main window.

Insertion effects can be applied to any one part, or the main output. This is in addition to whatever other System or Part effects may have been applied.

Part effects only apply to an individual part, as accessed from the group editor (described above).

Most of the effects will be familiar with the exception of AlienWah and DynFilter. These are ones that Paul Nasca designed and are quite different to any others. All of them except EQ (equalisation) have useful presets to give you starting points, and a set of controls so you can tailor them to your exact preferences – as usual, experiment!

Controllers

This button opens a window that allows you to define the ranges of various incoming MIDI control messages, and in some cases whether they are responded to at all. Taking the example of ‘VolRng’ (volume range), by default this is set so that the incoming MIDI level is reduced to approximately 75%. If it is turned up to maximum then the full range is passed through, and at minimum it is approximately half the range.

Controller settings are per part, so what you set on channel 4 (say) will have no effect on any others.

Scales

Probably of less interest to most users is the ability to set unique micro-tonal scales. The first item in the top menu bar ‘Scales’ will show the current settings, and enable you to change them. The default is the common Equal Temperament scale. Some of the settings are quite obvious, but for the rest you are advised to read up on differing scales. At the bottom of this window there are two import buttons that allow you to bring in recognised standard tunings and keyboard mappings.

Saving Work

Saving can only be done in the normal user areas of your file system, so it is a good idea to copy the default banks to your home directory. Depending on how Yoshimi was installed, banks may be in either of the following:
/usr/share/yoshimi
/usr/local/share/yoshimi

Use your normal file system commands to copy these, then click on Yoshimi’s top menu bar ‘Paths’, selecting ‘Bank Root Dirs’ then in the new window ‘Add root directory’. This will open a filer window for you to pick up and include the new set of banks. You can then click on the new root directory and make it the current one. In future the bank and instrument files will all be taken from there, so you can then add to these or change them while still keeping the originals intact.

Instruments

If you design a new instrument then obviously you will want to save it – although first you should give it a new name. To do this, in the main window click on the name field with the right hand mouse button and you will be presented with an editing window.

Once you have the name set you should decide whether you want to save the instrument as a separate entity or place it in one of the banks for easy reference and MIDI access.

To save it externally click on the top menu bar ‘Instruments’ then ‘Save External...’ and you will usually be offered the name you gave it, placed in your home directory. You can change this if you want to, but when re-loaded the edit window will have an extral line ‘Derived from ...’ giving the name it was first saved as.

To save in one of the instrument banks, open the bank you want to save to, click on the ‘SAVE’ button, then on the slot where you want your new instrument placed.

What you have saved will be the definition of all the engines, and the kit (if used). This won’t include humanise controls as they belong to the part itself, not the instruments you load into it.

Patch Sets

These are a more complete structure and include all instruments in all parts, regardless of whether the parts are active on not. They also include part controllers, and all effects, along with volume, key shift/range etc. Additionally they include any scale changes you have made. From version 1.4.1 this also includes any Vectors that have been set up.

These are saved via the top menu ‘Patch Sets’ and you can save with whatever name you like. As soon as you do, you will notice that ‘Recent Sets...’ has now been activated, so you can quickly re-fetch this, and any other ones you manage.

State

The entire state of Yoshimi can also be saved. This includes all of the above, along with all your settings preferences. By default it will be saved in:
/home/{user}/.config/yoshimi/yoshimi.state

However, you can actually save different states wherever you like, and (like patch sets) a recent history list will be set up. From version 1.4.1 states now include Vectors.

Vectors

This is a feature that allows you to control up to four parts as a group via a MIDI joystick, or other two axis controller. The parts are arranged in columns rather than the familiar row of 1 to 16. However, managing these groups is done as a MIDI base channel and parallels up to 4 parts per channel. So in theory you could have 16 of these defined.

This has its own button near the top of the main window, and opens a new 'Vectors' window. Initially most of this is deactivated, but the base channel can already be set to the incoming channel (and part 'column') you want to respond to.

Vectors use CCs (Continuous Controllers) to make the actual changes, one for each axis.
As soon as you set an incoming X CC, the rest of the X controls become active, as well as the Y CC spinbox. Also, Yoshimi will be set for 32 parts if it is currently 16, and the required ones will be enabled and checked to ensure they are set to the base channel.

The two instrument name panels behave in the same way as the main parts one, in that clicking on them brings up the instrument selection window, and the features determine what action will be taken when the value of the incoming CC is changed.

The Y axis is similar, and if activated, Yoshimi will be set for 64 parts.

All changes made are immediately effective, but disabling them will not disable the underlying instruments, nor will it lower the number of available parts. This is done to protect other elements that may have already been been set up.

The options menu allows you to load and save complete vector sets, and 'save' will double check that you have a valid set! Recent vector sets can be re-fetched in the same way as patch sets, scales and states. Either loading or saving a vector set will write its name in the small panel alongside the 'Close' button.

Midi Learn

This enables you to ‘teach’ Yoshimi to respond to MIDI CC messages .

To learn, hold Ctrl while right-clicking on any GUI control. There will be a pop-up window detailing the control you selected, or a message saying it's not learnable.

After that, if you were learning, the first physical controller you move, or CC message you send will be locked, and you'll see the GUI knob or slider move in sympathy with the physical control. The pop-up window will also disappear.

If you now use the 'Yoshimi' drop-down menu and click on 'MIDI Learn' you will see a new window displaying your recently learned controller. Along with a number of settings, you'll see text with precise details of this complete action.

There is also an 'activity' LED that flickers when the associated CC/channel is received, provided the line is not muted, or blocked by an earlier one.

MIDI-learn is unique in that the Master Reset button doesn’t clear the settings, as once set up most people want to keep it for an entire session. However, the editing window has a button to clear all of its current settings, along with the usual Load, Save and Recent options.

Other forms of Access

Yoshimi can also be started from the command line in a terminal window. Simply type in ‘yoshimi’ and you will be presented with a prompt ‘yoshimi >’. Typing in ‘?’ will give you a help list with minimum abbreviations capitalised. This mode of access gives you all of Yoshimi’s controls.

As well as normal MIDI CCs, program changes etc. very many settings can be changed via Non Registered Parameter Numbers (NRPN).

Further Information

Depending on how Yoshimi was installed, one of the following locations will give you some extra information, mostly in the form of plain text files:
/usr/share/doc/yoshimi
/usr/local/share/doc/yoshimi

Also, as well as a built in User Guide (found in the Yoshimi drop-down menu) a very detailed ‘Advanced User Manual’ has been built up by Chris at:
 https://github.com/ahlstromcj/yoshimi-doc

The Yoshimi support list archive is at: https://www.freelists.org/archive/yoshimi

From here there is a ‘Yoshimi’ link where you can subscribe to the list, and then post comments or questions. To post, email to yoshimi@freelists.org

Copyright © 2017-2023 Will J Godfrey	License: Creative Commons V4.0 Attribution, Share-Alike